## Slide 1: AUTOMATED DATA REDUCTION for the VIMOS INTEGRAL FIELD UNIT: how does it work?
A.Zanichelli, B.Garilli, M.Scodeggio, D.Rizzo

## Slide 2
IFU Head
IFU bundle and masks

## Slide 3
Why not use a “by hand” reduction?
Huge amount of data (6400 spectra from each exposure)
Complexity of IFU data
IFU data reduction requires dedicated algorithms (with respect to MOS or long slit):
cross-talk between spectra on the CCD
calibration of fiber relative transmission
sky determination and subtraction
Need an automatic, dedicated IFU Data Reduction Pipeline

## Slide 4
IFU First Light
one quadrant, raw
1600 spectra
Antennae Galaxy
LR Red, 5 min.
0.67 arcsec/fiber

## Slide 5
IFU Data Reduction
Part of the VIMOS Data Reduction Software (imaging, MOS, IFU), developed in C and Python languages.
As similar to VIMOS MOS data reduction as possible.
Works on single quadrant (4 images are acquired from each VIMOS exposure) up to Data Cube reconstruction.
Set of automatic procedures + some interactive functions.
As for MOS, makes use of auxiliary tables needed for reduction (optical distortion models & c.).

## Slide 6
The IFU Table
The IFU Table has been built according to IFU construction specifications.
For each fiber the IFU Table lists some fundamental parameters:
  correspondence between fiber position on the IFU head and spectrum on the detector
  fiber relative transmission measured by calibration procedures
  fiber profile parameters (X and Y FWHM of the spectrum on the CCD)

## Slide 7
IFU Data Reduction Steps
Sky determination and subtraction
Photometric Calibration
Build Data Cube
Build reconstructed 2D Image
4 quadrants
Bias and Flat Field correction
Cross Talk correction
Extract 2D spectrum
+
Wavelength calibration
Extract 1D spectrum
(no sky subtraction)
Relative transmission correction

## Slide 8
Cross-Talk Correction
Cross-Talk depends on:
spectral flux
fiber spatial profile
High density of spectra on the CCD
 flux “contamination” from adjacent spectra
For each fiber need to know fiber spatial profile parameters and shape
At each cross dispersion cut:
build spatial profile of each fiber
compare with measured module profile
apply flux correction

## Slide 9
Fiber Relative Transmission
Standard calibration of fiber relative transmission
  Image of twilight sky or image set in shift & stare mode
  fit sky lines + continuum (gaussian + 2 degrees polynomium)
  compute line flux and relative normalization
Options: Use only 5577A sky line (stable)
Use ALL possible sky lines and average
If needed: further refinement on each scientific frame
Different fibers have different transmission efficiencies
Relative transmission computed using sky lines

## Slide 10
    For each group:
    Collapse spectra in wavelength, build flux distribution and compute mode
    fibers having fluxes below the mode are considered sky
    combine sky fibers, build Mean Sky for the group and subtract
Sky subtraction
Stare observing mode: 400 spectra (work on pseudo-slits)
Group fibers according to FWHM along dispersion
  Shift & stare observing mode: work on single fiber spectra
    Combine exposures with rejection method
    Get a sky spectrum for each fiber and subtract

## Slide 11
Data Cube:
  all the four quadrants must have been reduced
  fully calibrated 1D spectra are rearranged according to the IFU Table, to allow a spatially coherent reconstruction of the observed sky region
2D reconstructed image:
  collapsing data cube in wavelength: whole grism spectral range or user-selected, smaller range
  use interpolation/drizzling techniques
IFU DRS Final Steps
Main IFU DRS products: set of 1D extracted, fully calibrated spectra + 3D data cube and 2D reconstructed image

## Slide 12
HDF South Through IFU

## Slide 13
Interactive Tools
Crowded fields: accurate sky subtraction
  automatic Data Reduction does not guarantee optimal sky subtraction
  on 2D reconstructed image, manually select fibers in sky regions
  build sky spectrum and subtract
Spectra Co-addition
  on 2D reconstructed image, check for “extended” objects
  spectra from microlenses falling on the same object are summed
Data Cube “slicing”
  select wavelength to get “monochromatic” image
  select range to get “narrow band” image

## Slide 14
Conclusions
IT WORKS…provided you have a very accurate calibration dataset!