## Slide 1
EFFI - E.S.O Fiber Fed Instrument
preliminary design concept and science case
culprits: O. Hainaut (ohainaut@eso.org)
A. Gilliotte (agilliot@eso.org)
E. Pompei (epompei@eso.org)

## Slide 2: Why bother? Stars and the like....
Planetary nebulae structure
HII regions
Extended stellar jets kinematics
SN extended envelope (see for example SN1987A, observed on Spiral A at AAT)
Milky Way studies
Local group galaxies

## Slide 3: Why bother? The extragalactic view...
Stellar kinematics and chemical abundances in elliptical galaxies: -determination of the velocity field; -mapping of abundance gradients; - shape of the galaxies
Stellar and gaseous kinematics of spiral galaxies: - bulge velocity maps; - detailed study of nuclear disks; - kinematics of bar and double bar systems; bar pattern speed
Stellar and gaseous kinematics of dwarfs and BCD galaxies: - detailed information on systems cosidered to be the relic of hierarchical formation of galaxies and on the distribution of the stellar population
Stellar and gaseous kinematics of compact groups, loose association of galaxies and galaxies in clusters: - how much the galactic potential is affected by interaction (coupled with HI and/or X-ray observations); -study of the inner galactic potential - activity level and physical conditions througout the emitting region

## Slide 4: Requirements, i.e. what we would like to have
Telescopes considered: ESO 3.6m or NTT (EMMI replacement)
Wide Field of View (F.O.V.): ~ 3'
Good sampling on the sky: 0.5"/fiber
Intermediate resolution: 5000
Wavelength coverage: 4860-5500 Å (Hb, Mg and Fe lines, [OIII]); 6300-6900 Å (Ha, [NII], [SII])
Complementary and competitive with other existing instruments
Maximize the use of duplication and modularity techniques, fixed configuration

## Slide 5: A possible solution might be....
Modular instrument, composed by many sub-units (37), each of them based on a fiber bundle: EFFI
input beam f ratio : 5.7 (for a 50mm fiber diameter, 3.4 for 30mm fiber diameter)
collimator f ratio: 5 (to allow for some FRD, would be 3 for the 30mm fiber)
image diameter: 30mm (2 CCD pixels)
camera f ratio: 5 (3), so to use a Littrow configuration for the spectrograph
re-imaging technique: focal reducer + macrolenses
in the preliminary design the dispersion is perpendicular to the main plane of the spectrograph, to minimize off-axis effect.
CCD detectors: 4k x 2k

## Slide 6: EFFI: schematic view
Left panel: schematic drawing of one sub-unit.
The configuration foreseen is a parabolic
collimator and a fixed plane grating.
Bottom panel: schematic 3D view of the optical path

## Slide 7: EFFI: arrangement on sky
Sinle spectrograph: one EFFI sub-unit, 1024 fibers on sky, ~20" FOV
Nine spectrographs: 9216 fibers on sky, ~70" FOV
Twenty-one spectrographs: 21504 fibers on sky,
~128" FOV
Final configuration: 37 spectrographs on sky,
37888 fibers on sky, 180" FOV (field diameter).
For all fields the inner circle marks the area with a
100% rotation coverage

## Slide 8: EFFI: data handling
a 100 Gb disk will contain ~ 160 raw spectra
removal of instrument signature (rotation effect included);
wavelength calibration;
data cube reconstruction
Basic idea: a computer dedicated to each spectrograph, plus one for the final assembly (in the final configuration)

## Slide 9: Or: image slicer? see: http://aig-www.dur.ac.uk/

## Slide 10: What now?
System choice: fibers vs slicer? - first one is "well" known and can be made relatively cheap; - second one is NOT cheap, but is interesting for the new tecnique and for the improved instrument compactness. Pb: how stable is the system in a seismic zone? would it be possible to obtain a wide FOV with a single slicer and multiple slits?
Software: pipeline is needed. Integration within ESO and/or other Working Groups?
Preliminary design review deadline: December 2002