## Slide 1
FLAMES/
GIRAFFE
** Euro3D kick-off meeting Jul. 2-4, 2002 **
GEPI -
L. Chemin
The ESO
instrument

## Slide 2
** ESO FLAMES Facility **
Australis cons.
(P.I.s : Taylor K.,
Colless M.)
FLAMES  Fibre Large Array Multi Element Spectrograph
ESO
(P.I. : Pasquini L.)
ESO
Paris Obs. (P.I. : Hammer F.)
Geneva Obs. (P.I. : Blecha A.)
+ Ital-FLAMES cons.
(P.I. : Cacciari C.)

## Slide 3
 Medium and High Resolution
R ~ 5500-30000
 3 obs. modes
MEDUSA
IFU
ARGUS
  = 370-900 nm
** Euro3D kick-off meeting Jul. 2-4, 2002 **
GIRAFFE
 f.o.v = 25 arcmin diameter

## Slide 4
25 25’
25’
MEDUSA mode

## Slide 5
 132 individual fibres for objects and sky
MEDUSA :
 Fibre  = 1.2” on the sky
 R ~ 5500 to 18000
 5 fibres for  calibration
** Euro3D kick-off meeting Jul. 2-4, 2002 **

## Slide 6
 15 deployable arrays
(20 fibres/bundle)
 5 individual  fibres
 Fibre  = 0.52” on the sky
 R ~ 9000 to 30000
 15 individual sky fibres
IFU(s) :
** Euro3D kick-off meeting Jul. 2-4, 2002 **

## Slide 8
ARGUS :
 1 single array of
22x14 channels (300 fibres)
 15 individual
sky fibres
 5 individual  fibres
 2 spatial sampling :
 R ~ 9000 to 30000
 = 0.52”
11.5”x7.3”
 = 0.3”
6.6”x4.2”
** Euro3D kick-off meeting Jul. 2-4, 2002 **

## Slide 9
Present status :
- commissioning phases at VLT
- first light
(see http://www.hq.eso.org/outreach/press-rel/pr-2002/pr-13-02.html)
Performances & limits :
 Total efficiency : ~ 8-10%
 Maximum sens. :  ~ 600 nm
(but also optimized in the blue part)
** Euro3D kick-off meeting Jul. 2-4, 2002 **
Following pictures kindly provided by ESO & Paris Obs. staffs.
1) view of the spectrograph; 2) fibres assembly at one OZPOZ plate;
3) view of OZPOZ at the telescope

## Slide 13
GIRAFFE data reduction & analysis soft.
 Developped at Geneva Obs. (+ Lausanne Univ.),
Paris Obs., ESO
(P.I. : A. Blecha)
 BLDRS :
- bias/dark subtraction, CRHs remov., SL adjust.
- spectra localization/extraction
- FF correction,  calibration
- sky subtraction & flux calibration
** Euro3D kick-off meeting Jul. 2-4, 2002 **

## Slide 14
 ADAS :
- Cross-Correlation function
- Projected rotational vel., metallicity (cool stars)
- Spectral indexes
- Equivalent width of absorption lines
- Image reconstruction
** Euro3D kick-off meeting Jul. 2-4, 2002 **

## Slide 15
 More informations :
- http://www.eso.org/instruments/flames
- http://giraobs.obspm.fr
- http://obswww.unige.ch/Instruments/GIRAFFE
** Euro3D kick-off meeting Jul. 2-4, 2002 **